## Slide 1
ENGINES
(Enabling Next GeneratIon NEtworks for broadcast Services)
Projects results highlights
Simulation and Validation
11 prototypes, from 15 contributing organisations
Test of TFS (Time and Frequency Slicing)
TFS consists of sending a large content streams (up to 200MB/s) across several discontinuous UHF frequencies . This allows to average the SNR and gain bitrate in channel with higher propagation loss .
MIMO channel modelling and validation of MIMO schemes for DVB-NGH
2x2 MIMO channel sounding in Helsinki (2010)
Simulation of MIMO coding schemes for DVB-NGH
Plug fests
Two Plug Fests carried out
  Oct.2011 (Barcelona) - “DVB-T2 Advanced Features Lab Test”
    Features tested: PAPR, Null FEFs, Multiple PLP, SFN, T2-MI.
  Sep./Dec.2012 (Barcelona/Rennes) - “NGH-Ph.1 Lab Test”
    Features tested: T2-Lite, Mixed T2-Base/T2-Lite, SFN, SC-OFDM.
Datapilot
DVB-T
modulator
PA
PA
Tx0
Tx1
VP
Antenna
HP
Antenna
BBC R&D MIMO Modulator
Inv
Backend
Backend
Transmit Side
Splitter
EB
Channel Recorder
BBC
MIMO Receiver
Real-time
Channel Display
RF Frontend
RF Frontend
Control
Laptop
Receive Side
Rx0
Rx0
Rx1
Rx1
Cross-polar
Application Antenna
2x2 MIMO
Channel Sounding
Channel
Measurement campaigns
Prototypes
Test of the SC-OFDM platform
SC-OFDM test platform in MERCE Rennes
Validation of the satellite component for DVB-NGH
Thomson Broadcast DVB-T2 transmitter
Teamcast DVB-T2 modulator
Teamcast DVB-T2 demodulator
Mier DVB-T2 transmitter
Mier DVB-T2 gapfiller
LaSalle DVB-T2 Gateway
Enensys DVB-T2 Gateway
Two Measurements Campaigns carried out
  Nov.2011(Barcelona) - “DVB-T2 Advanced Features Field Trials”
    Features tested: Multiple PLP.
  Sep./Oct.2012 (Barcelona) - “T2-Lite Field Trials”
    Features tested: T2-Lite, Mixed T2-Base/T2-Lite, SFN